## Slide 1: Sobel Edge Detection on FPGA
Shahbaz Hassan Khan Malik
California State University Northridge
ECE 524 - Fall 2022

## Slide 2: Order of presentation
Edge detection
  Edge detection
  Sobel Edge detection
  Convolution
Image processing on FPGA
  Line buffers
Implementation and results
Future

## Slide 3: Edge Detection
It is used in Image Processing for enhancing boundaries of an image
Edges in image are areas where there is a sudden change in intensity

## Slide 4: Edge Detection
There are various Edge detection methods (Laplacian, Sobel, Roberts, Canny)
We will be using Sobel Edge Detection for this project

## Slide 5: Sobel Edge Detection
It uses two matrices to find the gradient of the image intensity at each pixel
These kernels find vertical and horizontal edges
We perform 2D convolution on the image
-1 | 0 | +1
-2 | 0 | +2
-1 | 0 | +2
-1 | -2 | -1
0 | 0 | 0
+1 | +2 | +1

## Slide 6: Convolution
100 | 100 | 100 | 100
100 | 100 | 100 | 100
100 | 100 | 200 | 100
100 | 100 | 100 | 100
100 | 100 | 100 | 100
-1 | 0 | 1
-2 | 0 | 2
-1 | 0 | 1
*
Image Kernel

## Slide 7: Convolution
100 | 100 | 100 | 100
100 | 100 | 100 | 100
100 | 100 | 200 | 100
100 | 100 | 100 | 100
100 | 100 | 100 | 100
*

-1*100 | 0*100 | 1*100 | 100
-2*100 | 0*100 | 2*100 | 100
-1*100 | 0*100 | 1*200 | 100
100 | 100 | 100 | 100
100 | 100 | 100 | 100
Image Kernel Convolution
-1 | 0 | 1
-2 | 0 | 2
-1 | 0 | 1

## Slide 8: Convolution
100 | 100 | 100 | 100
100 | 100 | 100 | 100
100 | 100 | 200 | 100
100 | 100 | 100 | 100
100 | 100 | 100 | 100
*

-1*100 | 0*100 | 1*100 | 100
-2*100 | 0*100 | 2*100 | 100
-1*100 | 0*100 | 1*200 | 100
100 | 100 | 100 | 100
100 | 100 | 100 | 100
Image Kernel Convolution
-1 | 0 | 1
-2 | 0 | 2
-1 | 0 | 1
-100
100
-200
200
-100
200
+------
100

## Slide 9: Convolution
-1*100 | 0*100 | 1*100 | 100
-2*100 | 0*100 | 2*100 | 100
-1*100 | 0*100 | 1*200 | 100
100 | 100 | 100 | 100
100 | 100 | 100 | 100
Convolution Output Image
 | 100 |  | 
-100
100
-200
200
-100
200
+------
100

## Slide 10: Convolution
100 | 100 | 100 | 100
100 | 100 | 100 | 100
100 | 100 | 200 | 100
100 | 100 | 100 | 100
100 | 100 | 100 | 100
Convolution Output Image
New Value |  |  | 

## Slide 11: Convolution
100 | 100 | 100 | 100
100 | 100 | 100 | 100
100 | 100 | 200 | 100
100 | 100 | 100 | 100
100 | 100 | 100 | 100
Convolution Output Image
New Value | New Value |  | 

## Slide 12: Convolution
100 | 100 | 100 | 100
100 | 100 | 100 | 100
100 | 100 | 200 | 100
100 | 100 | 100 | 100
100 | 100 | 100 | 100
Convolution Output Image
New Value | New Value | New Value | 

## Slide 13: Convolution
100 | 100 | 100 | 100
100 | 100 | 100 | 100
100 | 100 | 200 | 100
100 | 100 | 100 | 100
100 | 100 | 100 | 100
Convolution Output Image
New Value | New Value | New Value | New Value

## Slide 14: Convolution
100 | 100 | 100 | 100
100 | 100 | 100 | 100
100 | 100 | 200 | 100
100 | 100 | 100 | 100
100 | 100 | 100 | 100
Convolution Output Image
New Value | New Value | New Value | New Value
 |  |  | New Value

## Slide 15: Convolution
100 | 100 | 100 | 100
100 | 100 | 100 | 100
100 | 100 | 200 | 100
100 | 100 | 100 | 100
100 | 100 | 100 | 100
Convolution Output Image
New Value | New Value | New Value | New Value
 |  | New Value | New Value

## Slide 16: Sobel Edge Detection Process
Image
*
*

## Slide 17: Image Processing in FPGA
We are working with 512x512 image, but we cannot have an i/o port that is 512x512 (two dimension)
It is also not practical to just send all the 262144 pixels of the image to the FPGA at once.
Storing the entire image on FPGA will utilize a lot of resources, which is not efficient. Unless the image is very small like 12x12

## Slide 18: Image Processing in FPGA
We will need to transform our design into some kind of a streaming algorithm
We can use a small memory to “buffer” the image
This small memory is known as a “Line Buffer” which stores one line of image
We will just send just enough pixels for processing the image instead of pushing the entire image at once
Reference: Image Processing using FPGA by Donald G. Bailey
Image pixels go in

## Slide 19: Image Processing in FPGA
Reference: Image Processing using FPGA by Donald G. Bailey
W9
100 | 100 | 100
100 | 100 | 100
100 | 100 | 200
100 | 100 | 100
Line Buffer
Line Buffer
Line Buffer
Line Buffer
Image
W8
W7
W4
W5
W6
W3
W2
W1

## Slide 20: Image Processing in FPGA
Reference: Image Processing using FPGA by Donald G. Bailey
W9
100 | 100 | 100
100 | 100 | 100
100 | 100 | 200
100 | 100 | 100
Line Buffer
Line Buffer
Line Buffer
Line Buffer
Image
W8
W7
W4
W5
W6
W3
W2
W1
W1 | W2 | W3
W4 | W5 | W6
W7 | W8 | W9
Sampling Window
K1 | K2 | K3
K4 | K5 | K6
K7 | K8 | K9
*

## Slide 21: Results
MATLAB: Convert image into 1D array  write the array into a text file
Vivado: Read the intensity values in test bench as the input to the design
MATLAB: Convert output text file back into an image

## Slide 22: Results

## Slide 23: Results

## Slide 24: Results
Sobel Canny

## Slide 25: Results

## Slide 26: Conclusion
Results can be improved by first applying a Gaussian low pass filter to remove noise and then applying the Sobel kernels
Design can be exported as an AXI IP and connected with DMA and Zynq SoC to create a fully hardware accelerated Sobel Edge Detection system [ECE 520]

## Slide 27: Thank You